## Slide 1
EN.525.670.81.SP21 - Machine Learning for Signal Processing
Machine Learning for Satellite Tracking
Team Members : Alec Briley, Christian Mielke, Michael Palasits
Date: April 27, 2021

## Slide 2: Overview
Introduction
Objective
Tasks
Results
Conclusions
Summary

## Slide 3: Introduction
Satellite tracking currently uses a physics based approach to estimate orbits.
The physics based approach is know to have built in errors due to unpredictable atmospheric conditions.
These errors can be large enough to cause collisions in the Low Earth Orbit (LEO) environment.
Proposed solution to satellite tracking errors is to use machine learning to model the orbit rather than a physics based approach to produce more accurate predictions.

## Slide 4: Introduction – cont.
Briefly state what has been accomplished in this project.

## Slide 5: Objective
  Machine learning will be used to model satellite orbits and compared to the physics propagation model (SGP4).
  Both models will then be compared to the truth data obtained from the International Laser Ranging Service (ILRS).
  Project will result in a more accurate orbital prediction model that can be used for third party satellite monitoring.

## Slide 6: Sensor
The data to be used for the machine learning approach will be in the Two Line Element (TLE) format. This format includes the following information.
  Epoch
  Orbit inclination
  Right ascension of the ascending node
  Eccentricity
  Argument of perigee
  Mean anomaly
  Mean motion
  Revolution number at epoch

## Slide 7: Sensor
The data to be used for the truth data will be in a modified version of Earth-centered, Earth-fixed (ECEF) format.
  Modified Julian Day
  Rectangular position characteristics (XYZ)

## Slide 8: Signal Capture
TLE data is acquired from US Strategic Command database and truth data is acquired from ILRS database.
The satellite Ajisai is used in this project due to the availability of truth data being limited to a smaller range of satellites than the TLE data.
Training data to be used in the machine learning algorithm is acquired in a six month block while test data is in a one month block

## Slide 9: Tasks
Describe the technical approach and goals in order to accomplish the project objective
  e.g. Sensor, Signal Capture, Data Conditioning, Feature Extraction, Modeling/Prediction
* Note: the detail discussion of each task should be presented in the Result/Conclusion sections later.

## Slide 10: Results
Describe the results obtained for each task
This is the main focus of the presentation. Positive or negative results should be presented with the details so that the reviewers will understand why the project is successful or runs into challenges.
Note: Plots and graphs are encouraged to use. However, do not just cut-and-paste the matlab output to presentation as is. The axis labels can be “enhanced” in the PowerPoint to help the reviewers to view the results.

## Slide 11: Conclusions
Based on the results of each task, you conclude whether the project objective has been accomplished.
Include lessons-learned and recommendations for future works.
This section is where the team convinces the reviewers that the project is well done, regardless the positive or the negative results.
The accomplishment of the project will be assessed in terms of the details of the task execution and the result analysis, the understanding of the challenges encountered during the project execution, the conclusion drawn from the results, and the plan for further studies in the area of the proposed project.

## Slide 12: Summary
Summarize the accomplishments of the course project and highlight the findings of the projects.